## Slide 1
MULTI-PURPOSE RESCUE AND INVESTIGATION ROBOT
İHSAN IŞIK
FEHIM TRNKA

## Slide 2: Bosnia and Herzegovina…

## Slide 3: BOSNIAN WAR
The Bosnian War was an international armed conflict that took place in Bosnia and Herzegovina between 1 March 1992 and 14 December 1995. The main belligerents were the forces of the Republic of Bosnia and Herzegovina and those of the self-proclaimed Bosnian Serb and Bosnian Croat entities within Bosnia and Herzegovina, Republika Srpska and Herzeg-Bosnia, who were led and supplied by Serbia and Croatia respectively.

## Slide 4: LAND MINES IN BOSNIA
As an after effect of the war land mines laid by all combatants remained leaving Bosnia and Herzegovina with one of the most severe land mine problems of the world.

## Slide 5
220,000 land mines and unexploded munitions remain scattered in 13,077 locations. A total of 1,755 km².
(3,4% of the Bosnia's whole territory)

## Slide 6
CASUALTIES
Land mine casualties in Bosnia and Herzegovina 1996-2009 |  |  | 
Year | Killed | Injured | Total
1996 | 110 | 552 | 662
1997 | 88 | 202 | 290
1998 | 60 | 80 | 149
1999 | 38 | 57 | 95
2000 | 35 | 65 | 100
2001 | 32 | 55 | 87
2002 | 26 | 46 | 72
2003 | 23 | 31 | 54
2004 | 16 | 27 | 43
2005 | 10 | 9 | 19
2006 | 18 | 17 | 35
2007 | 8 | 22 | 30
2008 | 19 | 20 | 39
2009 | 9 | 19 | 28
2010 | 6 | 8 | 14
Totals | 498 | 1,210 | 1,717
* “Land mine contamination in Bosnia and Herzegovina”, 10 August 2012, Wikipedia.‎

## Slide 7
Mine Sweeping…
The process of detecting mines in an area.

## Slide 8
METHODS
Manual detection with a metal detector
  The process of scanning the area with metal detectors.
Dogs
  Well-trained dogs that sniff out explosive chemicals like TNT in landmines.
Rats
  Giant pouched rats trained to sniff out chemicals like TNT in landmines. These rats are called HeroRATS. They have the advantage of being far lower mass than the typical human. They are less likely to set off small mines intended to injure or kill people, if the bomb-sniffing animal crosses directly over the top of a buried mine.
Mechanical clearance
  Special machines that effectively combine mine detection and removal into one operation. These machines consist of a special vehicle that is driven through the minefield, deliberately detonating the mines it drives over. These vehicles are designed to withstand the explosions with little damage. Some are operated directly with armor to protect the driver; some are operated under remote control.

## Slide 9
ACCIDENTS
12:55, 01/06/1999, Bosnia and Herzegovina/ Between Gajevi and Gornjani villages, RS SAMAC/BRVNIK Region. Full Report
  NAME REMOVED, surveyor
  severe Chest, severe Eye, severe Legs, LOST Toes, LOST Eye.
  NAME REMOVED, deminer
  severe Legs
  NAME REMOVED, surveyor
  FATAL
22/03/2008, Bosnia and Herzegovina/ Masici Village, Nr Goradze. Full Report
  NAME REMOVED
  FATAL
  NAME REMOVED
  FATAL
  NAME REMOVED
  FATAL
  NAME REMOVED, civilian
  Fragmentation Injuries
Sources:
DDAS Accident Report. Accident Number 207, 16/04/2004, http://www.ddasonline.com/PDF_files/DDASaccident207.pdf
DDAS Accident Report. Accident Number 717, 08/07/2011, http://www.ddasonline.com/PDF_files/DDASaccident717.pdf

## Slide 10
MP RAIR
MULTI-PURPOSE RESCUE AND INVESTIGATION ROBOT

## Slide 11
A SIX WHEELED, REMOTELY CONTROLLED VEHICLE CAPABLE OF MINE SWEEPING AND PINNING DOWN THEIR LOCATION…

## Slide 12: METAL DETECTOR
A Metal Detector for detecting metal in mines.
Product: Metal Detector
Operating Voltage: 9V (Battery)
Operates Under: Arduino

## Slide 13: WHEELS
3 independent wheels per side (six in total) increase traction. In other words, they provide better grip to the surface on rough terrain…
Product: LEGO, 56x26 Rubber Wheels

## Slide 14
NON-INDEPENDENT
INDEPENDENT
SOME WHEELS FAIL TO GET IN CONTACT WITH THE SURFACE.
ALL WHEELS ARE IN CONTACT WITH THE SURFACE. THUS, INCREASING TRACTION.
THIS MAKES IT EASIER FOR THE VEHICLE TO GO OVER ROCKS AND BUMPS ON THE SURFACE.

## Slide 15
CONVENTIONAL
MP RAIR
UNBALANCED. IT IS EASY TO IMAGINE THE DIFFICULTIES THE VEHICLE WOULD ENCOUNTER.
NO BALANCE ISSUES AS THERE ARE WHEELS IN CONTACT WITH THE SURFACE AT ALL POINTS

## Slide 16: WHEELS
3 independent wheels per side (six in total) increase traction. In other words, they provide better grip to the surface on rough terrain…
Product: LEGO, 56x26 Rubber Wheels

## Slide 17: WIRELESS CAMERA
A wireless camera attached to the front of the vehicle serves as a vision provider for the remote operator and is capable of capturing frames of the environment.
Product: HAMY, C-200
Operating Voltage: 5V
Operates Under: Controlling Device

## Slide 18: MOTORS
MP RAIR uses Modified Servo Motors rather than DC Motors for more torque at the cost of speed.
Product: Futaba, s3003 – Modified Mini Servo
Operating Voltage: 9V
Operates Under: Arduino Commands

## Slide 19: GPS
A GPS Module is used for location and speed information.
[Name/Brand], [Model]

## Slide 20: WIRELESS COMMUNICATION
Wireless Communication is handled by 2 nRF24L01modules connected to 2 Arduino Boards.
Product: [Name/Brand], nRF24L01
Operating Voltage: 3.3V

## Slide 21: PCB
The Printed Circuit Board (PCB) is the component that holds all these components together in a tidy, organized way providing the necessary wiring with each other and Arduino.
Product: Seeedstudio Fusion PCB
Designed in: Eagle CAD
Made in China

## Slide 22
PERFBOARD
PCB (Printed Circuit Board)
WIRES HANG AROUND AND THERE’RE A LOT OF MISCONNECTIONS ON SOLDER POINTS.
WIRES RUN THROUGH THE BOARD. THUS, AVOIDING UNORGANIZED WIRES HANGING AROUND. AND SINCE IN IS FACROTY PRODUCTION THE SOLDER POINTS ARE PERFECT.

## Slide 23: PCB
The Printed Circuit Board (PCB) is the component that holds all these components together in a tidy, organized way providing the necessary wiring with each other and Arduino.
Product: Seeedstudio Fusion PCB
Designed in: Eagle CAD
Made in China

## Slide 24: THE BRAIN – ARDUINO
Arduino is so called “the brain” of MP RAIR. It gets components work in harmony. It’s the thing that does the calculations and acts accordingly when necessary.
Product: Funduino, Mega
Microcontroller Chip: ATmega 2560
Language: C
Operating Voltage: 5V

## Slide 25: SCHEMATICS

## Slide 26: PROGRAMMING LANGUAGES
VISUAL STUDIO 12 - C#
ARDUINO IDE - C

## Slide 27
Arduino Mega
Metal Detector
Wireless
GPS
Motors
Controlling Device
Signals Arduino upon mine detection.
Sends commands to Arduino on how to move and interact. In the meantime it also receives information about mine coordinates, vehicle location…
Provides communication between master and robot.
Provides information such as coordinates and speed.
Provides movement to the vehicle according to commands issued by Arduino.
Arduino Mega
As the brain of the robot it acts upon data received from either the Metal Detector or the Wireless module by issuing commands to the motors or first obtaining GPS data and then sending those data to the master (Controlling Device) over Wireless.

## Slide 28
UPON MINE DETECTION
Mine Detected!
5 Volts are output to Arduino
Arduino is immediately alerted after receiving Voltage at its analog read pin and therefore goes on to obtain GPS data
Arduino receives GPS data and sends them to nRF24L01 (Wireless) to be sent to the Master.
Wireless Module sends these data to the Master letting it know about the mine and it’s location.
As the final step the Computer processes these data and pinnes the location of mine accordingly.
5V→

## Slide 29: Well…

## Slide 30
WHAT IF YOUR ROBOT PASSES RIGHT OVER THE MINE?

## Slide 31
ANTI-PERSONNEL AND ANTI-TANK MINES
?

## Slide 32
Pressure/Weight required to trigger a land mine is 11-35.3 pounds (5-16KG) for Anti-Personnel mines. As for Anti-Tank mines, they require even higher pressure as they are designed for tanks and vehicles. Our robot being only 1.1 Kilogram is very very unlikely to cause a mine explosion.
In the worst case, it’s still better than having a human set it off.
1.1 < 5
WHAT IF YOUR ROBOT PASSES RIGHT OVER THE MINE?

## Slide 33
NOT ALL MINES ARE MADE OF METAL.
AND YOU’RE USING A METAL DETECTOR…
Yes, at some point this is correct. However, according to Wikipedia; “Mines manufactured after the 1950s generally use plastic casings to hinder detection by electronic mine detectors. Some, referred to as Minimum metal mines, are constructed with as little metal as possible. Mines containing absolutely no metal have been produced, but are uncommon.”

## Slide 34
YOU MENTIONED SOME MACHINES THAT COMBINE MINE FINDING AND REMOVAL INTO ONE OPERATION EARLIER.
NOW, AREN’T THOSE BETTER THAN YOUR ROBOT?

## Slide 36: MP RAIR
  Low Cost (<$2000) ▲(with improved equipment)
  Portable/Small size ▲
  Less Energy consumption ▲
  Not capable of mine detonation ▼
  Easy to Use ▲
  Easy to obtain (Assemble/Make) ▲
MINE CLEARANCE MACHINES
VS
  High Cost (>$30000) ▼
  Huge size ▼
  More energy consumption ▼
  Capable of mine detonation ▲
  Skill required to use (Training) ▼
  Hard to obtain (Impossible for non-military personnel) ▼
▲ - UPSIDE
▼ - DOWNSIDE

## Slide 37
OPEN SOURCE
http://github.com/xiprox/sc_project_mp-rair

## Slide 38
REFERENCES AND SOURCES
“The Silent Menace: Landmines in Bosnia and Herzegovina”, 01 February 1998, INTERNATIONAL COMMITTEE OF THE RED CROSS.
http://www.icrc.org/eng/assets/files/other/silent-menace-bosnia-herzegovina-57jp32-010298.pdf
DDAS Accident Report. Accident Number 207, 16/04/2004.
http://www.ddasonline.com/PDF_files/DDASaccident207.pdf
DDAS Accident Report. Accident Number 717, 08/07/2011.
http://www.ddasonline.com/PDF_files/DDASaccident717.pdf
“Land mine contamination in Bosnia and Herzegovina”, 10 August 2012, Wikipedia.
http://en.wikipedia.org/wiki/Land_mine_contamination_in_Bosnia_and_Herzegovina
“Anti-personnel mine”, 25 April 2013, Wikipedia.
http://en.wikipedia.org/wiki/Anti-personnel_mine
“Bosnia and Herzegovina”, Landmine and Cluster Munition Monitor,
http://www.the-monitor.org/index.php/publications/display?url=lm/2006/bih.html
“Land mine”, 23 April 2013,‎ Wikipedia.
http://en.wikipedia.org/wiki/Land_mine
Bonsor, Kevin. "How Landmines Work" 19 June 2001. HowStuffWorks.com.
http://science.howstuffworks.com/landmine.htm
“Anti-Tank mine”, 22 February 2013, Wikipedia.
http://en.wikipedia.org/wiki/Anti-tank_mine
Gérald C. Cauderay (1993). Anti-Personnel Mines. International Review of the Red Cross, 33, pp 273-287. doi:10.1017/S0020860400080530.
“Demining”, 30 April 2013, Wikipedia.
http://en.wikipedia.org/wiki/Demining
“Minimum Metal Mine”, 8 February 2013, Wikipedia.
http://en.wikipedia.org/wiki/Minimum_metal_mine

## Slide 39
http://www.schrc.net/mp_rair
mprair@schrc.net

## Slide 40
Questions??